The things I had to do to compile for pico 2

- Renamed the f:\dev\tools\pico-sdk-master directory
- Cloned the pico-sdk master from the Raspberry Pi GitHub site
- In CmakeLists.txt added the PICO Board type:
  - set(PICO_BOARD pico)
- in parrot_main.c I needed to add include hardware/clocks.h
  - This is because set_sys_clock_khz has been moved
- Delete the entire contents of the \build directory

Those changes enabled me to recompile for pico1 / rp2040

When I changed the board type to pico2 it initially failed in the function alarm_in_us

- Changed
  - #define ALARM_IRQ TIMER_IRQ_1
  - to
  - #define ALARM_IRQ TIMER1_IRQ_1

To avoid problems in the future I added an #if to parrot.h

#if PICO_RP2040
    #define ALARM_IRQ TIMER_IRQ_1
#elif PICO_RP2350
    #define ALARM_IRQ TIMER1_IRQ_1
#endif

It then compiled OK, and the board booted, and I can use the PICO_BOARD setting in CMakeLists.txt to switch between the board types.

During initial testing, some functions do appear to work – eg the Audio in and out seem OK, as does the ext_clock input, though I am not getting any delayed signal at all, which makes me think that the PSRAM isn’t functioning.

Checked on Ian Scott’s GitHub, and there was a discussion that pointed to a missing gpio init in psram_spi.pio

    pio_gpio_init(pio, pin_miso);

This gets it *much* closer to working, though I’m not convinced about things like the switches.

The wet/dry balance pot is altering the volume of the dry signal, so the ADC seems to be OK.

Definitely some detailed hardware testing required, and I need to build a hardware test harness, but the initial steps are quite encouraging.

Testing results

The * / - switch doesn’t work. Presumably due to the pull-down bug. I am pulling it up to +3.3v, so using the internal pull-down resistor. Safest approach would be to use internal pull-up, and switch to GND

8-Way rotary switch with BCD Encoder works fine, and no internasl pull-up or -down resistors required

Sync / Free switch switches to Ground * works fine (though could do with a de-bounce

Algorithm falls foul of the GPIO Bug, but I’m considering an 8-Way algorithm switch anyway so it’ll get fixed via that. For testing purposes I added external 4k7 pull-down resistors, which fixed the Algorithm switch for testing purposes.

Feedback and Clock speed pots are wired back to front, though that is simply one instruction to reverse them in code, so not important.