Camberwell Parrot - Items that need fixing for a Rev-2 board

- Need to be agnostic to the RP2350 pull-down bug. Note and deal with any/all inputs that currently use pull-down.

This means use pull-up inputs where possible, and switch them to Ground externally, maybe remove all pull-up or -down resistors from inputs where driven by Eg MC14532 – need to experiment to see if they really need them

- Connect the clock LED directly to the Clock output port rather than a dedicated LED output.

This will win back another GPIO Pin, which should mean that we can use an 8-way algorithm switch

- Use a 7805 regulator in DPAK package with better ground heatsink

- reverse the connections to the feedback pot so that it increases as you turn it clockwise

- reverse the connections to the Clock Speed pot so that speed increases as you turn it clockwise!!

- turn the 8-Way switches 90 degrees so that the knobs point upwards

- turn the input gain pot 180 degrees so that flat side is in the correct orientation

- move the LED closer to the clock output.

- Check for PSRAM Pin-compatibility with the RP2350 Stamps

Software re-design considerations

- Could do with de-bouncing the Divisor switch, as it bounces terribly